## Slide 1
Impact of First Detections on Interferometer Design
David Reitze
LIGO Laboratory
California Institute of Technology
For the LIGO Scientific Collaboration
LIGO-G1601517-v2
LIGO Hanford Observatory
GR21, Columbia University, NYC, July 12, 2016
Notes: Thank the organizers for inviting me to give a presentation!

## Slide 2: What We Learned from the First Detections
Abbott, et al. ,LIGO Scientific Collaboration and Virgo Collaboration, “Binary Black Hole Mergers in the first Advanced LIGO Observing Run”, arXiv:1606.04856.

## Slide 3: Impacts on Interferometer Design?
Broadly speaking, this is really two questions:
How should we focus commissioning efforts to evolve toward Advanced LIGO design sensitivity?
How should we design upgrades to Advanced and new detectors based on first detections?
Ask question from the perspective of frequency
  ‘Low Frequency’ is ~ 20-200 Hz; ‘High Frequency’ is 200 – 2000 Hz
(Caveat: we’ve only seen two (or three) events of one class of source…)

## Slide 4: Commissioning Advanced LIGO Toward Design Sensitivity
LIGO-Virgo’s two (or three) binary black hole mergers provide an existence proof for the abundance of BBHs in the universe
  Inferred rate for stellar mass binary black hole mergers is in the range 9–240 Gpc-3yr-1
Heavier mass BBH systems merger at lower frequencies
GW150914 confirms existence of ‘heavy’ stellar mass black holes
Mass distribution? Heavier stellar mass BHs? Spin distribution? Formation mechanisms? Formation times?
Improve low frequency performance
For a given SNR, event parameter estimate improves with more cycles
 Improve low frequency performance
Abbott, et al. ,LIGO Scientific Collaboration and Virgo Collaboration, “Binary Black Hole Mergers in the first Advanced LIGO Observing Run”, arXiv:1606.04856.

## Slide 5: The perspective from other sources not yet detected?
The other compact binary mergers: binary neutron star, neutron star – black hole
  Modeling: NS tidal disruption frequencies occur in the kHz range
  Probing NS equation of state requires high SNR at merger frequencies above 1 kHz and/or a very large rate
Core Collapse Supernova
  Weak emitters; rates and waveforms uncertain
    Approximately every 30 to 100 years in our galaxy
  Generic burst concentrated around ~ 1 KHz
  We would have to be very lucky to detect with Advanced LIGO
Known Pulsars
  monochromatic (and weak) emitters at twice the rotational frequencies
  Best candidates Crab (~59.6 Hz) , Vela (22.4 Hz), J0537-6910 (124 Hz) –> low frequency
Stochastic GW background
  Primordial background from GWs orders of magnitude below sensitivities of current and probably even future detectors
  stochastic background made of all unresolvable BBH may be detectable already with current Advanced LIGO, Advanced Virgo, KAGRA detectors, but not until design sensitivity is reached, and then with a long integration time
Most potential scientific payoff in the near term comes from improving low frequency performance of the detector
Salvo Vitale:
https://dcc.ligo.org/LIGO-G1601471/public

## Slide 6: The Advanced LIGO Detector Sensitivity During O1
Abbott, et al. ,LIGO Scientific Collaboration and Virgo Collaboration, “GW150914: The Advanced LIGO Detectors in the Era of First Discoveries”, Phys. Rev. Lett. 116, 131103 (2016).
Arm Cavity Power Parm = 100 kW

## Slide 7: The Advanced LIGO Detector Sensitivity During O1
Abbott, et al. ,LIGO Scientific Collaboration and Virgo Collaboration, “GW150914: The Advanced LIGO Detectors in the Era of First Discoveries”, Phys. Rev. Lett. 116, 131103 (2016).
Arm Cavity Power Parm = 100 kW
Challenges:
- Complex light scattering mechanisms
- Squeezed film damping in the end test masses
- Pernicious mechanical interference
- Unkown noise in the Signal Recycling Cavity
Challenges:
High laser power
Parametric instabilities

## Slide 8: Mystery Low Frequency Noise!!
What’s known:
  Similar noise level between H1 and L1
    L1 shows additional bumps (maybe due to scattering)
  Relatively stationary
What’s not known:
  What causes it
  Exact spectral shape (not flat)
Already ruled out:
  ETM/ITM coating thermal or SUS thermal
  Simple light scattering mechanisms
  Suspension drive electronics
  Electric charge
Already ruled out: (cont’d)
  Sensing noise
  Laser noise (frequency, intensity, RFAM)
  Beam jitter
  Angular control noise
  Up-conversion
  Beamsplitter motion
  OMC related
  PEM related such as acoustic, seismic, magnetic, …
Still being investigated
  Complex light scattering mechanisms
  Squeezed film damping in the end test masses
  Mechanical interference
  Noise in the Signal Recycling Cavity (such as ITM/BS AR coatings)

## Slide 9: Problems with High Laser Power: Parametric Instability
Acoustic mode Optical mode
fm = 15,539 Hz
Theory: V. B. Braginsky, S. E. Strigin, and S. P. Vyatchanin, Phys. Lett. A 305, 111 (2002)
Experiment: C. Zhao, L. Ju, J. Degallaix, S. Gras, and D. G. Blair,
Phys. Rev. Lett. 94, 121102 (2005); M. Evans, et al., “Observation of Parametric Instability in Advanced LIGO”, Phys. Rev. Lett. 114, 161102 (2015).
mechanical mode
Q-factor
power in the
arm cavity
spatial overlap
Optical-mechanical mode
optical mode
gain
Acoustic mode
frequency
Parametric Gain:
Mirror
mass

## Slide 10: Observation of Parametric Instabilities in Advanced LIGO
(Parm = 50 kW)
ASD [counts/√Hz]
Frequency [Hz]
Time [min]
Anti-symmetric Port Output:
‘Ring Up’ Amplitude vs Time
How to Suppress Parametric Instabilities?
Thermally tuning the test mass radii of curvatures using ring heaters!
Active damping via electrostatic feedback through the reaction masses!
Passive damping via viscous acoustic mass damping (under development)??

## Slide 11: Sensitivity and Coincidence Goals for O2
Advanced LIGO’s second ‘O2’ run will begin in the Fall 2016
  Currently planning an early September start, but may slip into October to accommodate needed commissioning
Total planned run duration is 6 months
  Planned as a split run: 3 month + 3 month with 1-2 month commissioning break in early 2017
We expect a 15% – 25% sensitivity improvement over LIGO’s first observing run
  Comes primarily from increasing laser power from 20 to 50W  > 90 MPc binary neutron star inspiral range
  Low frequency (30-100 Hz) noises not well understood; no expected gains in that region for O2
  Still, an increase in BBH event rate of 1.5 – 2X
Aim for > 50% L1+H1 coincidence duty cycle (by comparison, we achieved 43% in O1)
2013 aLIGO Sensitivity Projections
2016 O1 Sensitivity, O2 Projection
O1; 75 Mpc BNS
O2; 90 Mpc BNS
aLIGO Design; 188 Mpc BNS

## Slide 12: Sensitivity and Coincidence Goals for O2
Advanced LIGO’s second ‘O2’ run will begin in the Fall 2016
  Currently planning an early September start, but may slip into October to accommodate needed commissioning
Total planned run duration is 6 months
  Planned as a split run: 3 month + 3 month with 1-2 month commissioning break in early 2017
We expect a 15% – 25% sensitivity improvement over LIGO’s first observing run
  Comes primarily from increasing laser power from 20 to 50W  > 90 MPc binary neutron star inspiral range
  Low frequency (30-100 Hz) noises not well understood; no expected gains in that region for O2
  Still, an increase in BBH event rate of 1.5 – 2X
Aim for > 50% L1+H1 coincidence duty cycle (by comparison, we achieved 43% in O1)
2013 aLIGO Sensitivity Projections
2016 O1 Sensitivity, O2 Projection
O1; 75 Mpc BNS
O2; 90 Mpc BNS
aLIGO Design; 188 Mpc BNS

## Slide 13
Impact of Discovery on Design of Upgraded Detectors

## Slide 14: A+: a Mid-Life Enhancement for Advanced LIGO
Science case for future major upgrade upgrade of LIGO currently under development
Near term: ‘A+’, a mid-scale upgrade of Advanced LIGO
  Improvements across all bands
  Sensitivity target: an average factor of ~1.6- 1.8 increase in range over Advanced LIGO design (up to 6X greater event rate)
Projected time scale for A+ operation: as early as 2023

## Slide 15: Squeezing: Reducing Shot Noise
Electromagnetic fields are quantized:
Quantum fluctuations exist in the vacuum state:
Aasi, et al., (LIGO Scientific Collaboration), Nature Physics, 7, 962 (2011); Nature Photonics 7 613 (2013).
Photodiode
Faraday
Isolator
Squeezed Vacuum
Source
Main Laser
PLL
x1
x2
Squeezed Vacuum
State
Amplitude squeezing
Phase
squeezing
Coherent State
ϕ
│E │
3.5 dB squeezing
(1.5X reduced noise)
2.1 dB squeezing
(1.27X reduced noise)
Typical noise without squeezing
Squeezing-enhanced sensitivity
Notes: Two demonstrations of squeezing!

## Slide 16: The Best of Both Worlds: Frequency Dependent Squeezing
PLL
Oelker, et al., “Audio-band Frequency-dependent Squeezing”, Phys. Rev. Lett. 116, 041102 (2016).
Notes: Walks through badness, and then sketch path to goodness

## Slide 17: Further Along: Future Detectors, Future Observatories
LIGO
Voyager
Two paths: exploiting the facility limits AND new facilities
Exploiting the facility limits:
  LIGO Voyager in the US
New facilities:
  Einstein Telescope in Europe
  Cosmic Explorer in the US
Planning and conceptual designs are underway

## Slide 18
Summary
Detections in LIGO’s O1 run supports optimistic stellar mass BBH rate estimates
Near term detection targets argue for better low frequency performance
Medium-scale ‘A+’ upgrade planned for Advanced LIGO
Science case for major upgrades will be informed by detections over the next few years
Acknowledgements:
  LIGO Scientific Collaboration
  Virgo Collaboration
  National Science Foundation
Thanks!